OWNERS MANUAL

MODEL:

THE ZEPHYR

Professional Cotton Candy Machine

PART NUMBER:

81011

115 volts, 60 hz

WARNING: Handling the cord on this product may expose you to lead, a chemical known to the State Of California to cause cancer and birth defects or other reproductive harm. WASH HANDS AFTER HANDLING.

Electrical ground is required on this appliance.

- Do not modify the power supply cord plug. If it does not fit the outlet, have a proper outlet installed by a qualified electrician.

- Do not use an extension cord with this appliance.

- Check with a qualified electrician if you are in doubt as to whether the appliance is properly grounded.

SAFETY INSTRUCTIONS

1.      Plug electrical cord into a certified electrical outlet with a corresponding voltage rating as listed on the machine model labels.

2.      Always unplug the electric cord when appliance is not in use and before cleaning, adjusting or maintaining this steamer. Do not operate with a damaged cord or plug or after the machine malfunctions, has been dropped or damaged. Use authorized service for examination, electrical or mechanical adjustment or repair.

3       This equipment will be HOT during use and for a short time after it is turned off, BE CAREFUL. To avoid burns, do not let bare skin touch hot surfaces. If provided, use handles when moving this appliance. Keep combustible materials away from appliance.

4.      Extreme caution is necessary when any appliance is used by or near children and whenever the appliance is left operating and unattended.

5.      This appliance is not intended for use in wet locations. Never locate appliance where it may fall into a water container.

6.      Do not insert or allow foreign objects to enter any ventilation or exhaust opening as this may cause an electrical shock, fire or damage to the appliance.

Benchmark USA Inc.  ●  25-J Brookfield Oaks Dr. ●  Greenville, SC 29607 ●  T: 864-312-5500  ●  F: 864-312-5505

Assembly Instructions

Figure 1

1.  Clean all parts of the machine before initial use.

2.  Assemble cover and bowl as shown in figure 1.

Wiring Diagram

L----------  Copper sheathed cable        T----------  Temperature limiter

M----------  80W Ac motor                   V----------  0~300V Ac voltage meter

Fu---------  Tubular fuse                       R----------  1000W heating plate

K----------   Main switch                       K1----------   Heating switch

Operating Instructions

- Plug unit into a properly grounded 120 volt power supply.

- Be sure to keep hands and loose clothing away from the spinning head.

- Fill spinning head with desired amount of sugar floss (1/8 cup = an average cone)

- Turn on POWER switch to spin head.

- Turn on HEAT switch.

- Once the head heats up floss will begin to melt and create cotton candy.

- Using a paper cone collect the cotton candy from the edges of the bowl in a circular motion.

- Repeat steps 3-7 until the desired amount of cotton candy has been produced.

- Turn OFF motor and heat switches when finished making cotton candy.

Page 2

Cleaning

- After a days use to remove the build up of sugar in the extractor head you MUST HEAT UP the extractor head to remove the screws and lid. Unplug unit.  Soak lid in water and wipe head clean with damp cloth.

- Remove bowl and wash with soap and water. Use wash cloth to wipe clean and let dry.

- Use a slightly damp, non-abrasive sponge or non-abrasive towel to wipe clean the outside of the unit, wipe with a non-abrasive towel to dry. Do not use excessive water when cleaning this unit.

Parts List

| Part # | Description |  | Part # | Description |
| --- | --- | --- | --- | --- |
| 81001 | Heating head |  | 81007 | Fuse 5A |
| 81002 | Electrical brush |  | 81008 | Fuse socket |
| 81003 | Motor |  | 81009 | Belt |
| 81004 | On/Off switch |  | 81010 | Temperature Limiter |
| 81005 | Bowl |  | 81012 | Spinning Shaft |
| 81006 | Bowl Mount Clamps |  | 81013 | Bubble Top Dome |

81001 Heating Head		      81002 Electrical Brush                          81003 Motor

81004 On/Off Switch		         81008 Fuse Socket                      81010 Temperature Limiter

To Order Parts Contact:

Benchmark USA Inc

25-J Brookfield Oaks Dr

Greenville, SC 29607

T: 864-312-5500

F: 864-312-5505

Email:  parts@benchmarkusainc.com

Page 3

Three Year Warranty

THE WARRANTY:

Benchmark USA warrants the original purchaser of new food equipment manufactured by Benchmark USA to be free from defects in material or workmanship  from the date of the original purchase for a period of three years.

WHO IS COVERED BY THIS WARRANTY:

The original purchaser who has provided proper proof of the original retail purchase and all other requested information.

WHAT IS WARRANTIED:

The obligation of Benchmark USA under this warranty is limited to the replacement of any parts or components that in the opinion of Benchmark USA are defective, F.O.B. the factory, or at any other location that Benchmark USA may designate.

WHAT VOIDS THE WARRANTY:

1.  Any piece of equipment that has been installed, operated or maintained inconsistently

with Benchmark USA operating instructions.

2.  Any  part  or  component  that has been modified, changed or altered from its original

configuration.

3.  Any   electrical  component   that   has  been   damaged  due  to  submergence  in  any

liquid.

4.  Any   part   or   component   that   has   been   subject   to  abuse,  misuse,  neglect  or

accidents.

EXTENT OF WARRANTY:

Any defective component, part or assembly returned to Benchmark USA will be replaced by Benchmark USA.  Benchmark USA will not be responsible for any expenses incurred by the customer under the terms of this warranty, nor shall it be responsible for any damages either consequential, special, contingent, or otherwise; or expenses or injury arising directly or indirectly from the use of a Benchmark USA product.  Any component, part or assembly returned to Benchmark USA must be returned at the customers expense along with proof of purchase.  Benchmark USA reserves the right to determine whether the terms of this warranty have been properly complied with.  In the event that the terms are not complied with, Benchmark USA shall be under no obligation to honor this warranty.

Benchmark USA Inc.  ●  25-J Brookfield Oaks Dr. ●  Greenville, SC 29607 ●  T: 864-312-5500  ●  F: 864-312-5505

# Text boxes

WARNING ELECTRICAL SHOCK HAZARD.

FAILURE TO FOLLOW THESE INSTRUCTIONS COULD RESULT IN SERIOUS INJURY OR DEATH.