OWNERS MANUAL

MODEL:

HOTDOG MINI CART

Hotdog Steamer

PART NUMBER:

60072

120 volts, 60 hz

WARNING: Handling the cord on this product may expose you to lead, a chemical known to the State Of California to cause cancer and birth defects or other reproductive harm. WASH HANDS AFTER HANDLING.

- Electrical ground is required on this appliance.

- Do not modify the power supply cord plug. If it does not fit the outlet, have a proper outlet installed by a qualified electrician.

- Do not use an extension cord with this appliance.

- Check with a qualified electrician if you are in doubt as to whether the appliance is properly grounded.

SAFETY INSTRUCTIONS

1.      Plug electrical cord into a certified electrical outlet with a corresponding voltage rating as listed on the machine model labels.

2.      Always unplug the electric cord when appliance is not in use and before cleaning, adjusting or maintaining this steamer. Do not operate with a damaged cord or plug or after the machine malfunctions, has been dropped or damaged. Use authorized service for examination, electrical or mechanical adjustment or repair.

3       This equipment will be HOT during use and for a short time after it is turned off  BE CAREFUL. To avoid burns, do not let bare skin touch hot surfaces. If provided, use handles when moving this appliance. Keep combustible materials away from appliance.

4.      Extreme caution is necessary when any appliance is used by or near children and whenever the appliance is left operating and unattended.

5.      This appliance is not intended for use in wet locations. Never locate appliance where it may fall into a water container.

Do not insert or allow foreign objects to enter any ventilation or exhaust opening as this may cause an electrical shock, fire or damage to the appliance.

CLEANING SAFETY INSTRUCTION

- Turn control off and unplug the power cord. Avoid splashing water onto control.

- Do not clean this appliance with a water jet or immerse in water or other liquid.

Benchmark USA Inc.  ●  25-J Brookfield Oaks Dr. ●  Greenville, SC 29607 ●  T: 864-312-5500  ●  F: 864-312-5505

ASSEMBLY

- Install the four legs into the threaded holes in the base.  Attach the two decorative wheels to the opposite side of the warmer from the control panel by removing the screws from the bottom plate (drawing# 4) and re-inserting through the hole on the wheel attachment bracket.

- Install the hotdog tray (perforated) and bun tray (solid) side by side in the reservoir.  Put a false bottom rack in each of the trays.  This will allow the hotdogs to cook faster and keep the buns from getting wet.  Place the domed lid over the Solid Bun Tray and the flat lid over the Hotdog Tray.

- Place the umbrella stand behind the warmer on the table surface.  Slide the umbrella shaft into the tube on the stand.  Position the umbrella as desired.

OPERATING INSTRUCTIONS

- Plug the machine into a properly grounded 120 volt power supply.

- Fill the reservoir with 7 quarts of water by removing the hotdog and bun trays from the machine and pouring water into the reservoir with a pitcher.  Using hot water will speed up the start-up time of the machine.  Fill the reservoir with water to the MAX line which is marked in the reservoir.  The warmer will hold a maximum of 7 quarts.

- Load the warmer with the desired amount of hotdogs by placing the Hotdogs in the Perforated Tray and the Buns in the Solid Tray.

- Turn on the “Master Switch” and set the thermostat to a maximum setting.  The machine should be producing steam in approximately 5-7 minutes (depending on water and room temperature).  You can adjust the thermostat according to your operating conditions.

- Once Steam is produced adjust the thermostat to 80-100 to COOK and 60-80 to HOLD.

- Once steam is produced a standard size hotdog should reach serving temperature in approximately 20-30 minutes.  Adjust the thermostat accordingly.  You will want the hotdogs to maintain at least 140 Degrees Fahrenheit before serving.

- CAUTION:  Use tongs to remove buns and hotdogs from the warmer as the product will be hot to the touch.

- IMPORTANT:   DO NOT LET THE WATER LEVEL IN THE RESERVOIR GET BELOW THE MINIMUM LINE.  Letting the water run low or out could damage the unit and void your warranty.  The minimum line represents 4 quarts of water.

CONDENSATION

- Cool air striking the warm steamer may cause moisture accumulation.  Protecting the unit from cool drafts of air will help prevent condensation.

- As the covers of the warmer are opened and closed some of the condensation may leak out from the under-sides of the lids.  This should be wiped up with a towel or rag.

Page 2

CLEANING THE MACHINE

- At the end of day:  Turn the machine off using the master switch.  Remove the lids, trays and false bottoms.   (caution:  the items will be hot unless you wait long enough to allow them to cool before removing!)  These items can be taken to a sink or dishwasher for cleaning.  Use a mild detergent and water to clean.

- Empty the remaining water in the reservoir by dumping it into a sink or drain. (caution: the water will be hot unless you allow sufficient cool-down time).  Clean the reservoir with a mild detergent and water.  Wipe down with a soft cloth.

- Wipe down the outside of the unit with a mild detergent and a soft cloth.

- After the components have been cleaned, re-assemble the machine as outlined above so you will be ready for the next usage.

ASSEMBLY

(complete parts list on page 7)

Page 3

WIRING DIAGRAM

ELECTRICAL SPECIFICATIONS

Volts:	120

Watts:	1200

Amps:	10.0

Hertz: 	 50/60

Page 4

ASSEMBLY

PARTS LIST

| Item | P/N | Description |
| --- | --- | --- |
| 1 | 6701 | Reservoir |
| 2 | 6702 | Warmer Body |
| 3 | 6703 | Front Plate |
| 4 | 6704 | Sheet Metal Screw |
| 6 | 6706 | Leg |
| 7 | 6707 | Element Spacer |
| 8 | 6708 | Acorn Nut |
| 10 | 6710 | Spacer tube |
| 11 | 6711 | Threaded Rod |
| 12 | 6712 | Bottom Aluminum Cover |
| 13 | 6713 | Jumper |
| 14 | 6714 | Terminal |
| 15 | 6715 | Terminal Screw |
| 17 | 6717 | Lock-washer |
| 18 | 6718 | Bolt |
| 26 | 6726 | Heating Element |
| 27 | 6727 | Heat plate |
| 28 | 6728 | Hold-down plate |
| 29 | 6729 | Bracket |
| 30 | 6730 | Element Lead |
| 31 | 6731 | Switch Cover |
| 32 | 6732 | Switch |
| 33 | 6733 | Plug |
| 34 | 6734 | Strain Relief |
| 35 | 6735 | LED Light |
| 37 | 6737 | Thermostat |
| 38 | 6738 | Thermostat knob |
| 40 | 6740 | Thermostat backer Plate |
| 41 | 6741 | Bolt |
| 42 | 6742 | Clamp |
| 43 | 6743 | Perforated Hotdog Tray |
| 44 | 6744 | Solid Pan |
| 45 | 6745 | Perforated Pan |
| 46 | 6746 | Flat Hotdog Lid |
| 47 | 6747 | Domed Bun Lid |
| 48 | 6748 | Umbrella |
| 49 | 6749 | Umbrella Stand |
| 50 | 6750 | Wheel |

To Order Parts Contact:

Benchmark USA, Inc.

25-J Brookfield Oaks Dr.

Greenville, SC 29607 USA

Tel:  877-432-5500

Fax:  864-312-5505

Email:  parts@benchmarkusainc.com

Page 7

Three Year Warranty

THE WARRANTY:

Benchmark USA warrants the original purchaser of new food equipment manufactured by Benchmark USA to be free from defects in material or workmanship  from the date of the original purchase for a period of three years.

WHO IS COVERED BY THIS WARRANTY:

The original purchaser who has provided proper proof of the original retail purchase and all other requested information.

WHAT IS WARRANTIED:

The obligation of Benchmark USA under this warranty is limited to the replacement of any parts or components that in the opinion of Benchmark USA are defective, F.O.B. the factory, or at any other location that Benchmark USA may designate.

WHAT VOIDS THE WARRANTY:

1.  Any piece of equipment that has been installed, operated or maintained inconsistently

with Benchmark USA operating instructions.

2.  Any  part  or  component  that has been modified, changed or altered from its original

configuration.

3.  Any   electrical  component   that   has  been   damaged  due  to  submergence  in  any

liquid.

4.  Any   part   or   component   that   has   been   subject   to  abuse,  misuse,  neglect  or

accidents.

EXTENT OF WARRANTY:

Any defective component, part or assembly returned to Benchmark USA will be replaced by Benchmark USA.  Benchmark USA will not be responsible for any expenses incurred by the customer under the terms of this warranty, nor shall it be responsible for any damages either consequential, special, contingent, or otherwise; or expenses or injury arising directly or indirectly from the use of a Benchmark USA product.  Any component, part or assembly returned to Benchmark USA must be returned at the customers expense along with proof of purchase.  Benchmark USA reserves the right to determine whether the terms of this warranty have been properly complied with.  In the event that the terms are not complied with, Benchmark USA shall be under no obligation to honor this warranty.

Benchmark USA Inc.  ●  25-J Brookfield Oaks Dr. ●  Greenville, SC 29607 ●  T: 864-312-5500  ●  F: 864-312-5505

# Text boxes

WARNING ELECTRICAL SHOCK HAZARD.

FAILURE TO FOLLOW THESE INSTRUCTIONS COULD RESULT IN SERIOUS INJURY OR DEATH.